J Bolton

Lab 8 Test Report

In this lab, I completed the following: the program counter subcircuit, the memory address register, the instruction register, the RAM, and part of the controller sequencer. Before the end of next lab I have to complete the controller/sequencer and all remaining test cases for it.

Program Counter

Counting
Cp is high, Ep is high, and CLR is high:
W Bus reads XXXX0000
One clock:
W Bus: XXXX0001
Two clocks:
W Bus: XXXX0010

Clearing
Cp is low, Ep is low, and CLR is low:
W Bus reads XXXX0000

Memory Address Register

Loading
W Bus: 00001011
Lm is low
One clock:
MAR output: 1011

Instruction Register

Loading
W Bus: 10101011
Li is low
One clock:
IR Bus output: 1011
IR C/S output: 1010

Clearing
CLR is high
IR Bus output: 0000
IR C/S output: 0000

Loading to MAR
IR Bus output: 1110
Lm is low, Li is high, Ei is low, one clock:
MAR output: 1110

RAM

PC to MAR to RAM
Goal: put RAM contents at memory address B (A9) onto output display.
1. Clear PC
2. Ep high, CP high
3. Clock 11 times.
4. W Bus lower nibble: 1011B = 11D = BH
5. Cp low, Lm low, 1 clock – MAR output = 1011
6. CE high, W-Bus: 1010 1001 = A9H
7. Lo low, 1 clock – Output display: 1010 1001 = A9H

Three cycle fetch intruction test
PC contains 0010
First clock – PC transferred to MAR
Second clock – PC incremented to 0011
(RAM contents at 0010 = ABH)