J Bolton – Computer Architecture, Spring
Sap-1s Design Document
Control Word
Size: 20 bits (only 17 are used, leaving room for expansion)
All control signals are active high for the sake of simplicity.
No-op is 00000
Left side
Left side (x8)	Right side (x12)
Cp Lp Ep Lm Le Ee Li Ei	X X X S- S+ Ts Ls Es Su Lu Eu Lo

Key:
Cp: Increment program counter.
Lp: Load into program counter.
Ep: Put program counter's value on the bus.
Lm: Load in the MAR.
Le: Load into memory.
Ee: Put memory contents onto the bus.
Li: Load into the IR
Ei: Put the contents of the IR onto the bus.
S-: Decrement stack.
S+: Increment stack.
Ts: Enable a test on the stack to see if it's 0000.
Ls: Load into the top of the stack.
Es: Put stack contents onto the bus.
Su: Make the ALU subtract rather than add.
Lu: Load a into the ALU.
Eu: Put ALU result onto the bus.
Lo: Load into output register.
X: Nothing. I'm leaving these spots reserved for expansion.

T-State Instructions
T-State is still only a max of 6 steps.
TODO: T-State starts over if it encounters the no-op, so commands that take 4 t-states will only go through 4 t-states.
The three fetch states are the same operations but with a different control word.
lda loads to the top of the stack.
add and sub no longer take a memory address, but access the top two items in the stack.
the alu contains two registers so that the data values that are being added can exist outside of the stack. If the alu operated directly on the stack without registers, then it couldn't also load back into the stack. One register is always automatically loading from the stack with every clock. This way we don't need a seventh t-state. The second register loads from the bus
[fetch]
T-state	Operation	Active control signals	Control word
T1	MAR ← PC	Ep, Lm	30000
T2	PC++	Cp	80000
T3	IR ← Mem.	Ee, Li	06000

load m
T-state	Operation	Active control signals	Control word
T4	MAR ← IR	Ei, Lm	11000
T5	Stack ←Mem.	Ee, Ls	04020
T6	Stack++	S+	00080

output
T-state	Operation	Active control signals	Control word
T4	Output ← Stack	Es, Lo	00011
T5	No-op	None	00000
T6	No-op	None	00000

halt is executed with a hardwired NAND gate in the IR and requires no control words.
add
T-state	Operation	Active control signals	Control word
T4	ALU ← Stack, Stack--	Lu, Es, S-	00114
T5	ALU ← Stack	Es, Lu	00014
T6	Stack ← ALU	Ls, Eu	00022

Cp Lp Ep Lm Le Ee Li Ei X X X S- S+ Ts Ls Es Su Lu Eu Lo
0 0 0 0 0 0 0 0 0 0 0 1 0 0 1 0 0 0 1 0
0 0 0 2 2

Load ALU, S--
Load ALU
Eu, Ls